## Slide 1
Materials & general instruction
Sandboil (ring levee)
Vertical stacking (with geotextile)
1a
3a
5a
1c
1d
2e
2a
2b
4
2c
1b
Basics of stacking
6
5b
Subsurface bearing capacity
3b
2d
3c
3b
layer 1
Empty part
Friction
Work instruction using sandbags for waterdefences
Version 02-08-2023
Notes: In de linker kolom staat uitleg over de materialen en algemene instructies.
In de rechter kolom de toepassingen in het veld.
1. Voor de persoonlijke veiligheid:
- Draag handschoenen voor het sjouwen van zandzakken.
- Draag veiligheidsschoenen om klemmen te voorkomen.
- Draag een helm in de buurt van machines.
2. Sta tegenover elkaar bij het doorgeven van zakken.
3. Denk na voordat je zandzakken stapelt. Bekijk de video.
4. Zandzakken hebben een formaat van gemiddeld 40x60 cm.
Vul deze maximaal voor 2/3 met zand. Het losse eind, de strik, is nodig om zakken in verband te stapelen.
Bind of naai de zakken dicht zodat het zand niet kan uitspoelen.
De afdichtstrop (tiewrap) moet ook een handbreedte ruimte boven het zand open laten.
Maximaal gewicht is 15 kg om het werken met zandzakken vol te kunnen houden.
Gebruik geen zakken die open zijn. Vul ze niet volledig: die zijn niet goed te vormen.
5. Gebruik zandzakken die in minimaal 1 richting wrijving of schuifweerstand hebben door de ruwe stof.
Leg die schuifweerstand haaks op de waterdruk.
6. Stapel zakken altijd in halfsteensverband.
De rijen naast elkaar verspringen een halve zak. De rijen bovenop elkaar ook per drie lagen.
Leg maximaal 3 rijen op elkaar van een bepaalde breedte.
Wordt de stapel hoger? Bouw dan van onderaf met een extra laag uit.
7, De zakken komen ‘kont op strik’. Dat betekent dat een volle onderkant op een lege bovenkant komt te liggen.
Loop de zakken goed aan voor stevigheid.
8. Loop bij het stapelen tegen een schuine zijde de kanten goed aan.
De strik ligt altijd aan de zijde van de stapeling. Niet tegen de zijkant.
9. Stapel zakken altijd in halfsteensverband. Ook de rijen naast elkaar verspringen een halve zak.
De zakken komen ‘kont op strik’. Dat betekent dat een volle onderkant op een lege bovenkant komt te liggen.
Op het eind van een rij stapel je deze netjes af zodat er geen losse strikken vrij liggen.
10. Stapel zakken op een stevige ondergrond.
Gebruik een geotextiel bij een zachte ondergrond. Deze moet wel water doorlaten.
11. Gebruik een waterdichte folie om een stapeling waterdicht te maken.
Laat de achterzijde open, zodat water dat er misschien toch in komt, er weer uit kan.
Zandzakken vol water gaan vervormen.
12 Niet doen:
Stapel zandzakken niet op rommel of zand. Het risico is lekkage.
Leg de strik niet naar het water. Het risico is losspoelen.
Stapel de zakken niet slordig en losjes. Het risico is wegzakken.
Sluit de achterzijde niet waterdicht af. Het risico is verzadiging met water en wegzakken.
Wissel zandzakken niet af met bigbags. Elke overgang tussen zandzak en bigbag is een zwakte.
13. Stapel een ring van zandzakken rond een wel waar zand uit komt.
Door de ring hoger te maken, ontstaat waterdruk in de ring.
Die druk remt het water dat uit de grond stroomt. Dit vertraagt het water. Het zand komt tot rust.
Stapel de ring zo hoog dat het water nog wel stroomt, maar er geen zand meer uit komt.
Maak daarvoor een lage uitstroomopening in de ring en leg daaronder zandzakken. Dit voorkomt erosie.

## Slide 2
Werkinstructie zandzakken leggen voor waterkeringen
Work instruction using sandbags for waterdefences
Versie 2022-06-07
1a. More information on Youtube or website ‘Wiki Emergency Response Flood Defenses’ (Dutch).
Explanation of the drawing: top view, side view, front view. Layers on top of each other, rows next to each other.
1b. Personal safety, wear:
Gloves for carrying sandbags.
Safety shoes for foot protection.
A helmet in the vicinity of (rotating) machines.
Rest, eat and drink on time.
1c. Size and filling
Sandbags have an average size of 40x60 cm.
Fill this up to 2/3 with sand. Bags that you fill completely do not shape well.
The max. weight is 15 kg to be able to keep working with sandbags.
Tie or seal the bags closed so that the sand cannot wash out. If binding or sealing is not possible: fold the top at an angle and place it under a bottom of a sandbag.
The sealing (or tie wrap) should leave a hand's width of space above the sand to shape the bag
The loose/empty end, the top, is needed to stack bags in a bandage.
1d. Shear resistance
Use sandbags made of rough fabric so that they do not slip or shift. The friction differs for every fabric.
Plastic bags must have friction or shear resistance in at least one direction.
2a. Passing on filled sandbags
Keep the bag close to your body.
Use your forearms like a forklift. Use long sleeves.
Stand facing each other when passing bags. Count on 1 person per meter of 'chain'. Stand in order of length.
2b. ‘Bottom on top’
The pockets come ‘bottom on top': put a full bottom on an empty top.
Therefore, do not let the bag fall, but put the bottom down first and place the top last.
2c. Walking on the sandbags
Walk on every layer of bags to improve strength. Not the last bag placed: you then press the sand into the empty top.
2d. ‘Half-brick’ and crosswise
Stack bags in a row in a ‘half-brick’ way: rows are staggered by half a bag.
Stack the end of a row neatly so that there are no loose flaps.
“Friction crosswise, stack crosswise”.“ Friction in one direction, pile in one direction”.
2e. Subsurface bearing capacity
Stack the sandbags on a firm surface.
Do not stack too much weight on a surface. It must not deform.
3a. Vertical stacking
The stack takes the form of a blunt pyramid.
Place the first row at the water side in such a way that you can always expand inwards.
Place a maximum of two layers of a certain width on top of each other.
Stack every two layers with half a bag in width.
Does the stack needs to be higher?  build from the bottom up with an extra layer.
3b. Do not allow overflowing or overtopping
Overflow or overtopping cause the stack to collapse at the rear.
3c. Seal with foil
A stack can lose strength if it becomes saturated with water.
Use a waterproof geotextile to make a stack watertight on the water side.
Leave the back open so that water can always escape.
4. Sand boil
Water can flow under a levee through a layer of sand.
If the water flows fast enough, it takes grains of sand with it. The flow can be slowed down by back-pressure.
To do this, stack a ring of sandbags around a sandboil where sand flows out. You make a kind of bathtub.
By making the ring higher, water pressure is created inside the ring. The outflow determines the height.
That water pressure slows down the water flowing out of the ground. The sand settles.
Stack the ring so high that the water still flows, but no more sand comes out. So a minimum height.
Make an outflow opening in the ring and place sandbags under it. This prevents erosion.
5a. Ditch
Use a wading suit and life jacket.
When stacking against a sloping side, walk on the sides well.
The flap is always on the side of the stack. Not against the side.
5b. Wall
Stack the bags firmly against the wall. Walk on it well.
Pack the wall all around, at least by a distance that corresponds to half the width (1/2 W) of the stack (W).
6. Don’ts
Do not stack sandbags on top of rubbish or sand. The risk of leakage increases.
Do not put the top towards the water. The risk of loosening increases.
Do not stack the bags sloppily and loosely. The risk is that the pile will sink.
Do not alternate sandbags with bigbags. Any transition between sandbag and bigbag is a weakness and can leak.