## Slide 1: Work instruction / guide How to use sand bags? Booklet complementary to presentation: ‘train the trainer’.

## Slide 2
This booklet in pdf is intended as a description to '2 Work Instruction on how to use sandbags presentation.ppt'.
Preparation:
Wear personal protective equipment.
Put four sandbags on the ground or table: 2x2, so 2 side by side, 2 high. You will need this to explain the drawing and the concepts of layers/rows.
Then you can use those four sandbags to show how to stack ‘bottom on the top’.
If you have plastic bags, lay out 2 of them to show the sliding resistance.

## Slide 3
Hello.
My name is……………
I am going to give you an instruction on how to use sandbags.
I do this using pictures.
Sometimes I grab a sandbag to demonstrate.

## Slide 4: Explanation drawing
planview
side
front
layer
Bott-om
flap
row
1
2
3
4

## Slide 5
Preparation:
Put four sandbags on the ground: 2x2, so 2 side by side, 2 vertically.
And point out what you mean.
In this presentation we use pictures. Explanation:
On the left picture you see the sandbag drawn from above. The full part we call the bottom, the empty part the top.
The second picture is of a sandbag drawn on its side.
The third from the front or back.
‘Layers’ we use for sandbags on top of each other, vertically. Like layers of snow.
‘Rows’ lay next to each other, side by side. Like rows of chairs.

## Slide 6: Safety

## Slide 7
For personal safety
Wear:
Gloves for carrying sandbags.
Safety shoes for foot protection.
A helmet in the vicinity of (rotating) machines.
Rest, eat and drink on time.

## Slide 8: Size and filling
1/3
2/3
max 15 kg
approx. 0,4 m.
Ca. 0,6 m.
100 %

## Slide 9
Size and filling
Sandbags have an average size of 40x60 cm.
Fill this up to 2/3 with sand. Bags that you have filled completely are not good for shaping or lifting.
The max. weight is 15 kg to be able to keep working with sandbags.
When the bag gets wet, it gets heavier.
Tie or sew the bags closed so that the sand cannot wash out.
The sealing (or tie wrap) should leave a hand's width of space above the sand to shape the bag correctly.
The loose/empty end, the top, is needed to stack bags interconnected.
If binding or sealing is not possible: fold the top at an angle and place it under a bottom of another sandbag.
Never use loose ends in a stack. No full bags either.

## Slide 10: Shear resistance
friction

## Slide 11
Preparation
Have two plastic bags ready to show.
Shear resistance
Use sandbags made of rough fabric so that they do not slip or shift.
Plastic bags must have friction or shear resistance in at least one direction.
(Let this be heard by sliding two bags lengthwise and crosswise)
Place the shear resistance at the right angles to the water pressure.
“Friction crosswise, stack crosswise”
“Friction in one direction, pile in one direction”

## Slide 12: Passing on
1 pers. / m1
…….

## Slide 13
Passing on
Stand facing each other when passing bags. This is better for your back.
Count on 1 person per meter of 'chain'. Stand in order of length.
Keep the bag close to your body.
Work RVP:
  Rest on time.
  Variety of tasks.
  Proactively indicate what is needed: do not leave the chain unnecessarily with their hands full.

## Slide 14: ‘Bottom on top’
empty part

## Slide 15
‘Bottom on top’
The pockets come ‘bottom on top': put a full bottom on an empty top.
Show this too. Use the four bags for this.
Grab a bag by the top and bottom.
Lower it to the ground.
Hold the top the longest so that the bottom lands on the floor first.

## Slide 16: Walking on the sandbags

## Slide 17
Walking on the sandbags
Walk on the layer of sandbags to improve strength, every layer.
Not the last bag placed: you then press the sand into the empty flap.

## Slide 18: ‘Half-brick’
1/2
layer 1

## Slide 19
‘Half-brick’
Stack bags in a row in a ‘half-brick’ way: rows are staggered by half a bag.
You can demonstrate this
Stack the end of a row firmly so that there are no loose tops.

## Slide 20: Crosswise
friction crosswise, layers crosswise
friction one direction, layers one direction

## Slide 21
Crosswise
The alternation of layers on top of each other depends on the friction of the fabric.
You can feel it by sliding bags over each other.
“Friction crosswise, stack crosswise”
“Friction in one direction, pile in one direction”
You can demonstrate this.

## Slide 22: Subsurface bearing capacity
solid

## Slide 23
Subsurface bearing capacity
Stack the sandbags on a firm surface.
Also take into account the strength of the slopes.
The stack of sandbags should not be too heavy for the subsoil. It can sink under the weight.

## Slide 24: Vertical stacking
max. 2 layers
½
½
etc.
^
^
>> etc.
+1

## Slide 25
Vertical stacking
The stack takes the form of a blunt pyramid.
The bottom layer is always one bag wider than the second layer.
Place a maximum of two layers of a certain width on top of each other.
For example, you get: 3 on the bottom, 2 on top, 2 on top, 1 on top, 1 on top.
Stack every two layers with half a bag in width. The aspect ratio will be approximately 1:2.
Does the stack needs to be higher? Then build from the bottom up with an extra layer.

## Slide 26: Overflow and overtopping

## Slide 27
Overflow and overtopping
The stack becomes saturated due to overflowing or overtopping water.
This causes the back row of the bags to 'flow' and move downwards at an angle.
 make the pile high enough to stop all the waves.

## Slide 28: Seal with geotextile
geotextile
no geotextile

## Slide 29
Seal with geotextile
A stack can lose strength if it becomes saturated with water.
Use a waterproof geotextile to make a stack watertight on the water side.
Place the geotextile corresponding with the flow, in a way that the water does not flow around the overlap.
Place the film under the front row of bags only. Otherwise the stack may slide on the geotextile.
Fold the geotextile over it, like a hood.
Place the loose top under a sandbag and put a bag on top so that the top cannot be moved by the wind.
Leave the back open so that water can always escape.

## Slide 30
outlet
Ring levee
Sandboil

## Slide 31
Sandboil
Water can flow under a levee through a layer of sand and bubbling up a hole.
If the water flows fast enough, it takes grains of sand with it.
The flow can be slowed down by back-pressure.
To do this, stack a ring of sandbags around a sandboil where sand flows out. You make a kind of bathtub.
By making the ring higher, water pressure is created inside the ring. The outflow determines the height.
That water pressure slows down the water flowing out of the ground. The sand settles.
Stack the ring so high that the water still flows, but no more sand comes out. So a minimum height.
Make an outflow opening in the ring and place sandbags under it. This prevents erosion.

## Slide 32: Ditch
ditch

## Slide 33
Here you see a ditch in a cross-section.
Ditch
Use a wading suit and life jacket.
When stacking against a sloping side, walk on the sides well.
The top is always on the side of the stack. Not against the side.

## Slide 34: Wall
wall
½ W
W

## Slide 35
Wall
You can see a wall from above.
Stack the bags tightly against the wall. Walk on it well.
Pack the wall all around, at least by a distance that corresponds to half the width (1/2 W) of the stack (W).

## Slide 36
a.
b.
c.
d.
Don’ts

## Slide 37
Don’ts
Do not stack sandbags on top of rubbish or sand. The risk of leakage increases.
Do not put the top towards the water. The risk of loosening increases.
Do not stack the bags sloppily and loosely. The risk is that the pile will sink.
Do not alternate sandbags with bigbags. Any transition between sandbag and bigbag is a weakness and can leak.