## Slide 1: Work instruction / guide How to use sandbags? Short version for (field) instructions to volunteers

## Slide 2: Target group
Instructors give this explanation to the people stacking the sandbags:
with the drawings and the explanation they can understand how to stack correctly.
Note for the instructor
Watch the instruction video and/or follow the 'train the trainer' instruction.
Print this presentation as a PDF in A3 format, landscape and double-sided along the short side and put a ring binder on the short side.
(A2 is too small for explanation to a group).
A sturdy back helps to display the booklet.
With the help of this printed presentation you can give instructions to small groups (approx. 10 people).
The booklet is made so that on your side read the instruction text while you turn the image to the group.
You can do this with the PowerPoint. Then remove the text slides.
Keep it short: limit yourself to the instructional text.
Make sure you wear the personal protective equipment yourself.
Have a few bags ready to show you.

## Slide 3
This blank page is for printing the booklet.
The images and instructional texts will then be clearly visible to the instructor and volunteers.

## Slide 4: Safety and working conditions
1 pers. / m1
…….

## Slide 5: Instruction text
For personal safety, wear:
Gloves for carrying sandbags.
Safety shoes for foot protection.
A helmet in the vicinity of (rotating) machines.
Rest, eat and drink on time.
Passing on heavy sandbags
Keep the bag close to your body.
You can pass the bags on bent forearms, like a forklift.
Stand facing each other when passing on bags. Count on 1 person per meter of 'chain'.
Communicate well about the pace of picking up and putting down the bags.
Work RVP:
  Rest on time.
  Variety of tasks.
  Proactively indicate what is needed: do not leave the chain unnecessarily with their hands full.

## Slide 6: ‘Half-brick’, friction
1/2
layer 1

## Slide 7
‘Half-brick’ and crosswise
Rows:
Put the row in ‘half-brick’: the next row is offset by half a sandbag.
The bags should be bottom on top': put a full bottom on an empty top.
Turn every last bag of a row, do not leave a loose top sticking out.
Walk on the bags gently to ensure a good fit.
Next layer:
If the fiber of the bag has cross resistance, stack the layers crosswise.
If the fiber of the bag gives resistance in one direction, stack the layers in one direction.
Put the new layer firmly again like the first layer. Walk on the bags each layer.

## Slide 8: Vertical stacking
max. 2 layers
½
½
etc.
^
^
>> etc.
+1
foil
No foil

## Slide 9
Vertical stacking
The stack takes the form of a blunt pyramid.
Place a maximum of two layers of a certain width on top of each other.
Stack every two layers with half a bag in width.
Does the stack needs to be higher? Then build from the bottom up with an extra layer.
Make the stack so high that no water can overflow or overtop it. Otherwise the rear will sink further and further.
Seal with geotextile
A stack can lose strength if it becomes saturated with water.
Use a waterproof geotextile to make a stack watertight on the water side.
Place the geotextile under the front row of bags only.
Tuck the top of the geotextile under a row of sandbags to prevent it from blowing away.
Leave the back open so that water can always escape.

## Slide 10
outlet
Ring levee
Sandboil

## Slide 11
Sandboil
Water can flow under a levee through a layer of sand.
If the water flows fast enough, it takes grains of sand with it. You can slow down the flow by counter-pressure with water.
Therefore, stack a ring of sandbags around a well where sand comes out.
By making the ring higher, water pressure is created inside the ring.
That water pressure slows down the water flowing out of the ground. The sand settles.
Stack the ring so high that the water still flows, but no more sand comes out.
You determine the water height with the outflow opening in the ring.
Place sandbags underneath. This prevents erosion.

## Slide 12
a.
b.
c.
d.
Don’ts

## Slide 13
Don’ts
Do not stack sandbags on top of rubbish or sand. The risk of leakage increases.
Do not put the top towards the water. The risk of loosening increases.
Do not stack the bags sloppily and loosely. The risk is that the stack will sink.
Do not alternate sandbags with bigbags. Any transition between sandbag and bigbag is a weakness and can leak.